## Slide 1: A01_CNSL
All the load cases can meet the target.
Overview
PAMCRASH Version: | 2022
CAD Version: | 2024.11.20、2024.12.20、2025.01.08

## Slide 2: A01_CNSL
All reports of load cases summary
CNSL | Load case | RT | Remark
Basic version | 1.1. Static center console compression | OK | All the load cases can meet the target.
 | 1.2. Static center armrest compression | OK | All the load cases can meet the target.
 | 3.1. Noise, vibration, and harshness (NVH) | OK | 1st global modal= 33.2Hz > 28Hz, and it can meet the target.
 | 3.5. Rear impact | OK | All components have no faults. The CNSL components are not separate.

## Slide 3: A01_CNSL - Basic Version
All cases in this page can meet the target in final.
Static center console compression result overview
Point Number | V00 |  | 
 | CAE Result | Less than yield stress | Status
ASP01 | 1.54mm | YES | OK
ASP02 | 1.81mm | YES | OK
ASP03 | 1.86mm | YES | OK
ASP04 | 1.23mm | YES | OK
ASP05 | 1.59mm | YES | OK
ASP06 | 1.87mm | YES | OK
ASP07 | 1.90mm | YES | OK
ASP08 | 1.09mm | YES | OK
ASP09 | 2.75mm | YES | OK
ASP10 | 0.45mm | YES | OK
ASP11 | 1.28mm | YES | OK
ASP12 | 1.18mm | YES | OK
Point | X/mm | Y/mm | Z/mm
ASP01 | 2535.045 | -137.608 | 1494.316
ASP02 | 2690.554 | -123.977 | 1477.510
ASP03 | 2824.061 | -114.450 | 1464.855
ASP04 | 2963.569 | -114.971 | 1413.031
ASP05 | 3101.078 | -109.881 | 1402.665
ASP06 | 3250.269 | -106.533 | 1391.180
ASP07 | 3262.292 | -108.134 | 1336.864
ASP08 | 3116.555 | -112.396 | 1268.835
ASP09 | 3256.077 | -113.973 | 1169.689
ASP10 | 3138.611 | -118.225 | 1184.385
ASP11 | 2905.215 | -115.373 | 1381.423
ASP12 | 3030.039 | -113.218 | 1364.742
Y-direction
Force:150N(P01~19)
(1st row center console)
displacement<3mm
Force:75N (P20~27)
(2nd row center console)
displacement<3mm Ø80mm
1、No plastic deformation
2、No breakage
3、Fastening point must not fail

## Slide 4: A01_CNSL - Basic Version
All cases in this page can meet the target in final.
Static center console compression result overview
Point Number | V00 |  | 
 | CAE Result | Less than yield stress | Status
ASP13 | 1.21mm | YES | OK
ASP14 | 0.65mm | YES | OK
ASP15 | 1.57mm | YES | OK
ASP16 | 0.86mm | YES | OK
ASP17 | 1.08mm | YES | OK
ASP18 | 0.67mm | YES | OK
ASP19 | 0.98mm | YES | OK
ASP20 | 2.12mm | YES | OK
ASP21 | 1.89mm | YES | OK
ASP22 | 0.80mm | YES | OK
ASP23 | 0.86mm | YES | OK
ASP24 | 0.39mm | YES | OK
Point | X/mm | Y/mm | Z/mm
ASP13 | 2412.711 | -138.939 | 1362.510
ASP14 | 2599.746 | -124.334 | 1406.647
ASP15 | 2771.253 | -117.059 | 1385.309
ASP16 | 2844.594 | -100.964 | 1283.317
ASP17 | 2563.777 | -130.397 | 1144.582
ASP18 | 2678.176 | -126.445 | 1154.408
ASP19 | 2791.921 | -122.969 | 1154.372
ASP20 | 2082.390 | -127.470 | 1157.922
ASP21 | 2175.111 | -125.739 | 1157.610
ASP22 | 2340.405 | -137.200 | 1101.211
ASP23 | 2367.481 | -148.397 | 1266.894
ASP24 | 2431.458 | -134.923 | 1130.722
Y-direction
Force:150N(P01~19)
(1st row center console)
displacement<3mm
Force:75N (P20~27)
(2nd row center console)
displacement<3mm Ø80mm
1、No plastic deformation
2、No breakage
3、Fastening point must not fail

## Slide 5: A01_CNSL - Basic Version
All cases in this page can meet the target in final.
Static center console compression result overview
Point Number | V00 |  | 
 | CAE Result | Less than yield stress | Status
ASP25 | 0.62mm | YES | OK
ASP26 | 1.30mm | YES | OK
ASP27 | 0.31mm | YES | OK
ASP28 | 2.55mm | YES | OK
ASP29 | 2.28mm | YES | OK
ASP30 | 0.59mm | YES | OK
ASP31 | 0.59mm | YES | OK
ASP32 | 1.33mm | YES | OK
ASP33 | 0.45mm | YES | OK
Point | X/mm | Y/mm | Z/mm
ASP25 | 2882.108 | -121.226 | 1138.765
ASP26 | 2981.156 | -111.337 | 1265.768
ASP27 | 3028.640 | -118.926 | 1182.003
ASP28 | 3261.404 | 0.000 | 1080.026
ASP29 | 3324.451 | 0.000 | 1127.180
ASP30 | 3242.127 | -29.099 | 1145.652
ASP31 | 3242.127 | 29.099 | 1145.652
ASP32 | 3319.266 | 0.000 | 1281.725
ASP33 | 3320.631 | 0.000 | 1339.854
1、No plastic deformation
2、No breakage
3、Fastening point must not fail
Y-direction
Force:75N (P20~27)
(2nd row center console)
displacement<3mm Ø80mm
X-direction
Force:150N(P28~33)
displacement<3mm
Ø40mm

## Slide 6: A01_CNSL - Basic Version
All cases in this page can meet the target in final.
Static center console compression result overview
Point Number | CAE Result | Less than yield stress | Status
ASP34 | 4.45mm | YES | OK
ASP35 | 4.90mm | YES | OK
ASP36 | 4.87mm | YES | OK
ASP37 | 3.95mm | YES | OK
ASP38 | 1.93mm | YES | OK
ASP39 | 1.94mm | YES | OK
ASP40 | 3.72mm | YES | OK
ASP41 | 3.71mm | YES | OK
ASP42 | 3.36mm | YES | OK
Point | X/mm | Y/mm | Z/mm
ASP34 | 3260.106 | 0.000 | 1433.087
ASP35 | 3085.980 | 62.300 | 1443.459
ASP36 | 3085.980 | -62.300 | 1443.459
ASP37 | 3149.991 | 0.000 | 1445.166
ASP38 | 2790.179 | 39.025 | 1366.178
ASP39 | 2790.179 | -39.026 | 1366.178
ASP40 | 2610.661 | 45.696 | 1472.142
ASP41 | 2610.661 | -45.696 | 1472.142
ASP42 | 2709.509 | 0.000 | 1480.828
Z-direction
Force:300N(P34~45)
displacement<5mm
Ø40mm Force:300N(P46)
displacement<5mm
Ø80mm
1、No plastic deformation
2、No breakage
3、Fastening point must not fail

## Slide 7: A01_CNSL - Basic Version
All cases in this page can meet the target in final.
Static center console compression result overview
Z-direction
Force:300N(P34~45)
displacement<5mm
Ø40mm Force:300N(P46)
displacement<5mm
Ø80mm
1、No plastic deformation
2、No breakage
3、Fastening point must not fail
Point Number | V00 |  | 
 | CAE Result | Less than yield stress | Status
ASP43 | 4.68mm | YES | OK
ASP44 | 2.03mm | YES | OK
ASP45 | 2.05mm | YES | OK
ASP46 | 2.66mm | YES | OK
ASP47 100N | 3.40mm | YES | NOK
ASP47 150N | 4.77mm | YES | OK
Point | X/mm | Y/mm | Z/mm
ASP43 | 2639.044 | 0.000 | 1185.990
ASP44 | 2603.682 | 117.233 | 1213.335
ASP45 | 2603.020 | -114.033 | 1213.336
ASP46 | 3357.858 | 0.000 | 1170.792
ASP47 | 2487.910 | 0.000 | 1505.724
Z-direction
Force:100N(P47)
displacement<3mm
Ø25mm Force:150N(P47)
Less than yield stress
Ø25mm

## Slide 8: A01_CNSL - Basic Version
All cases in this page can meet the target in final.
Static center armrest compression result overview
Point Number | V00 |  | 
 | CAE Result | Less than yield stress | Status
ASP48 | 1.53mm | YES | OK
ASP49 | 3.57mm | YES | OK
ASP50 | 3.53mm | YES | OK
ASP51 | 3.13mm | YES | OK
ASP52 | 3.14mm | YES | OK
ASP53 | 6.10mm | YES | OK
ASP54 | 8.34mm | YES | OK
ASP55 | 5.10mm | NO | NOK
1、No plastic deformation
2、No breakage
3、Fastening point must not fail
150N*X-direction
displacement<30mm
300N*Y-direction
displacement<15mm
800N*Z-direction
displacement<30mm
Ø80mm
Close
X
Y
Z
Point | X/mm | Y/mm | Z/mm
ASP48 | 3317.248 | 0.000 | 1405.983
ASP49 | 3236.032 | 107.935 | 1408.464
ASP50 | 3236.031 | -107.931 | 1408.463
ASP51 | 2919.264 | 117.053 | 1434.417
ASP52 | 2921.257 | -116.999 | 1434.257
ASP53 | 3254.574 | 0.000 | 1433.921
ASP54 | 3072.751 | 0.000 | 1451.760
ASP55 | 2935.410 | 0.000 | 1462.649

## Slide 9: A01_CNSL - Basic Version
All cases in this page can meet the target in final.
Static center armrest compression result overview
Point Number | V00 |  | 
 | CAE Result | Less than yield stress | Status
ASP56 | 1.78mm | YES | OK
ASP57 | 1.77mm | YES | OK
ASP58 | 1.90mm | YES | OK
ASP59 | 26.64mm | NO | NOK
ASP60 | 2.07mm | YES | OK
ASP61 | 1.72mm | YES | OK
ASP62 | 1.41mm | YES | OK
ASP63 | 32.24mm | NO | NOK
1、No plastic deformation
2、No breakage
3、Fastening point must not fail
150N*X-direction
(extended position)
displacement<30mm
150N*Y-direction
(extended position)
displacement<30mm
150N*Z-direction
(extended position)
displacement<30mm
Ø80mm
Open
X
Y
Z
Point | X/mm | Y/mm | Z/mm
ASP56 | 3329.782 | -65.257 | 1542.465
ASP57 | 2904.725 | -88.192 | 1601.232
ASP58 | 3114.749 | -74.680 | 1618.065
ASP59 | 3114.765 | -56.195 | 1576.067
ASP60 | 3329.782 | 65.257 | 1542.465
ASP61 | 2904.725 | 88.192 | 1601.232
ASP62 | 3114.749 | 74.680 | 1618.066
ASP63 | 3114.765 | 56.195 | 1576.067

## Slide 10: A01_CNSL - Basic Version
1st global modal= 33.2Hz > 28Hz, and it can meet the target.
Results overview of NVH analysis
3.1 NVH analysis
Global Modal |  | Target | CAE Result | Status
CNSL | 1st | Natural Frequency > 28Hz | 33.9Hz | OK
 | 2nd |  | 46.7Hz | 
IP+CNSL | 1st | Natural Frequency > 28Hz | 33.2Hz | OK
 | 2nd |  | 49.6Hz | 

## Slide 11: VW416/9CM B-SUV CNSL - Basic Version
The load case of Rear Impact can meet the target.
Results overview of Rear Impact
3.5 Rear Impact
Loading: 30g Sine wave
Target:
1、No failure of parts.
2、Components must not separate.
Loading Direction: Global -X
Temperature: 23℃
Load case | Target | V00 | 
 |  | CAE Result | Status
Rear Impact | 1、No failure of parts. | All components have no faults. | OK
 | 2、Components must not separate. | The CNSL components are not separate. | OK