## Slide 1: A01_IP
All load case summary
Load case | OK | NOK | Remark
1.1 Static dashboard compression test | X |  | All of the points can meet the target.
1.2 Static pressure test of FID and ABT | Acceptable |  | All of points can meet the displacement target, but when loading force is 400N, individual elements in FID、ABT and IP occurred plastic strain.
1.3. Static glove compartment compression test | X |  | The glove box is not damaged, it can meet the target.
2.1 Head impact | X |  | All of the points can meet the target.
3.1 NVH analysis | X |  | 1st global modal of IP is 35.1 Hz > 35Hz.
3.4 Rear impact | X |  | The IP structure and Wrap-around trim bracket is complete, the connection points between IP and CCB have not fallen off, there are only individual welding columns and ribs have detached, and there are no parts flying out.
3.6. Image stability of FID and ABT | X |  | All response points can meet the target,
3.7 PAB Deployment RT&HT&LT | Acceptable |  | Upper and lower bracket is complete at RT、HT、LT, There are minor damage in topper cover at RT、HT、LT; Speaker cover、air outlet trim panel and upper atmosphere light cover have not fallen off, and front glass has on failure at three temperatures.

## Slide 2: A01_IP
All points can meet the target.
Static dashboard compression test result overview
Point Number | Load | Target | CAE Result | Status
ASP01 | 400N oval-R17 | Stiffness value> 40N/mm | 115.27N/mm | OK
ASP02 |  |  | 145.45N/mm | OK
ASP03 |  |  | 186.92N/mm | OK
ASP04 |  |  | 136.05N/mm | OK
ASP05 | 400N ø25mm |  | 285.71N/mm | OK
ASP06 |  |  | 243.90N/mm | OK
ASP07 |  |  | 220.99N/mm | OK
ASP08 |  |  | 182.65N/mm | OK
ASP09 |  |  | 191.39N/mm | OK
ASP10 |  |  | 232.56N/mm | OK
ASP11 | 400N oval-R17 |  | 400.00N/mm | OK
ASP12 |  |  | 248.45N/mm | OK
Point Number | Load | Target | CAE Result | Status
ASP13 | 400N oval-R17 | Stiffness value> 40N/mm | 141.34N/mm | OK
ASP14 |  |  | 158.10N/mm | OK
ASP15 |  |  | 213.90N/mm | OK
ASP01
ASP02
ASP04
ASP05
ASP06
ASP07
ASP08
ASP09
ASP10
ASP11
ASP12
ASP13
ASP14
ASP15

## Slide 3: A01_IP
All points can meet the target.
Static dashboard compression test result overview
Point Number | Load | Target | CAE Result | Status
ASP16 | 300N oval-R17 | Stiffness value> 30N/mm | 545.45/mm | OK
ASP17 |  |  | 428.57N/mm | OK
ASP18 |  |  | 428.57N/mm | OK
ASP19 |  |  | 370.37N/mm | OK
ASP20 |  |  | 789.47N/mm | OK
ASP21 |  |  | 1304.48N/mm | OK
ASP22 |  |  | 750.00N/mm | OK
ASP23 |  |  | 857.14N/mm | OK
ASP24 |  |  | 157.07N/mm | OK
ASP25 |  |  | 600.00N/mm | OK
ASP26 |  |  | 638.30N/mm | OK
ASP27 |  |  | 85.96N/mm | OK
Point Number | Load | Target | CAE Result | Status
ASP28 | 300N oval-R17 | Stiffness value> 30N/mm | 87.72N/mm | OK
ASP16
II
ASP17
ASP18
ASP19
ASP20
ASP21
ASP22
ASP23
ASP24
ASP25
ASP26
ASP27
ASP28

## Slide 4: A01_IP
All points can meet the target.
Static dashboard compression test result overview
Point Number | Load | Target | CAE Result | Status
ASP29 | 200N oval-R17 | Stiffness value> 15N/mm | 400.00N/mm | OK
ASP30 |  |  | 240.96N/mm | OK
ASP31 |  |  | 192.31N/mm | OK
ASP32 |  |  | 155.04N/mm | OK
ASP33 |  |  | 110.50N/mm | OK
ASP34 |  |  | 327.87N/mm | OK
ASP35 |  |  | 122.70N/mm | OK
ASP36 |  |  | 434.78N/mm | OK
ASP37 |  |  | 289.86N/mm | OK
ASP38 |  |  | 357.14N/mm | OK
ASP39 |  |  | 162.60N/mm | OK
ASP40 |  |  | 127.39N/mm | OK
ASP29
III
ASP30
ASP31
ASP32
ASP33
ASP34
ASP35
ASP36
ASP37
ASP38
ASP39
ASP40
ASP41
ASP42
ASP43
ASP44
ASP45
ASP46
ASP47
ASP48
ASP49

## Slide 5: A01_IP
All points can meet the target.
Static dashboard compression test result overview
Point Number | Load | Target | CAE Result | Status
ASP41 | 200N oval-R17 | Stiffness value> 15N/mm | 384.62N/mm | OK
ASP42 |  |  | 289.86N/mm | OK
ASP43 |  |  | 454.55N/mm | OK
ASP44 |  |  | 476.19N/mm | OK
ASP45 |  |  | 117.65N/mm | OK
ASP46 |  |  | 152.67N/mm | OK
ASP47 |  |  | 416.67N/mm | OK
ASP48 |  |  | 444.44N/mm | OK
ASP49 |  |  | 408.16N/mm | OK
ASP29
III
ASP30
ASP31
ASP32
ASP33
ASP34
ASP35
ASP36
ASP37
ASP38
ASP39
ASP40
ASP41
ASP42
ASP43
ASP44
ASP45
ASP46
ASP47
ASP48
ASP49

## Slide 6: A01_IP
Load case review
Loading Force:
F=100N,Dispacement < 3mm
F=400N,Displacement < 15mm
Target: No plastic strain
Loading Direction: Normal
Temperature: 23℃
1.2. Static pressure test of FID and ABT

## Slide 7: A01_IP
When loading force is 100N , all points can meet the target.
Static pressure test of FID result overview
Point Number | Load | Target | CAE Result | Plastic Strain (FID) | Plastic Strain (IP) | Status
ASP01 | 100N ø25mm | Displacement<3mm No plastic strain | 1.77mm | 0.000 | 0.000 | OK
ASP02 |  |  | 1.16mm | 0.000 | 0.000 | OK
ASP03 |  |  | 1.79mm | 0.000 | 0.000 | OK
ASP04 |  |  | 1.71mm | 0.000 | 0.000 | OK
ASP05 | 400N ø25 |  | 1.11mm | 0.000 | 0.000 | OK
ASP06 |  |  | 1.72mm | 0.000 | 0.000 | OK

## Slide 8: A01_IP
When loading force is 100N , all points can meet the target.
Static pressure test of ABT result overview
Point Number | Load | Target | CAE Result | Plastic Strain (ABT) | Plastic Strain (IP) | Status
ASP07 | 100N ø25mm | Displacement<3mm No plastic strain | 1.62mm | 0.000 | 0.000 | OK
ASP08 |  |  | 1.74mm | 0.000 | 0.000 | OK
ASP09 |  |  | 1.47mm | 0.000 | 0.000 | OK
ASP10 |  |  | 1.94mm | 0.000 | 0.000 | OK
ASP11 | 400N ø25 |  | 1.53mm | 0.000 | 0.000 | OK
ASP12 |  |  | 1.73mm | 0.000 | 0.000 | OK
ASP13 |  |  | 2.05mm | 0.000 | 0.000 | OK
ASP14 |  |  | 2.05mm | 0.000 | 0.000 | OK
ASP15 |  |  | 1.89mm | 0.000 | 0.000 | OK
ASP16 |  |  | 1.63mm | 0.000 | 0.000 | OK

## Slide 9: A01_IP
When loading force is 400N , there has individual elements in FID occurred plastic strain at ASP04、ASP06, there is low possibility to occur plastic deformation.
ASP01-03 and ASP05 can meet the target.
Static pressure test of FID result overview
Point Number | Load | Target | CAE Result | Plastic Strain (FID) | Plastic Strain (IP) | Status
ASP01 | 400N ø25mm | Displacement<15mm No plastic strain | 5.00mm | 0.000 | 0.000 | OK
ASP02 |  |  | 3.84mm | 0.000 | 0.000 | OK
ASP03 |  |  | 6.01mm | 0.000 | 0.000 | OK
ASP04 |  |  | 7.24mm | 0.001 | 0.000 | Acceptable
ASP05 | 400N ø25 |  | 4.85mm | 0.000 | 0.000 | OK
ASP06 |  |  | 6.99mm | 0.001 | 0.000 | Acceptable

## Slide 10: A01_IP
When loading force is 400N, there has no plastic strain occurred in IP, but individual elements in ABT occurred plastic strain at ASP07-08, ASP10-11, ASP14, there is low possibility to occur plastic deformation.
ASP09, ASP12-13 and ASP15-16 can meet the target.
Static pressure test of ABT result overview
Point Number | Load | Target | CAE Result | Plastic Strain (ABT) | Plastic Strain (IP) | Status
ASP07 | 400N ø25mm | Displacement<15mm No plastic strain | 5.91mm | 0.001 | 0.000 | Acceptable
ASP08 |  |  | 6.29mm | 0.001 | 0.000 | Acceptable
ASP09 |  |  | 5.17mm | 0.000 | 0.000 | OK
ASP10 |  |  | 6.78mm | 0.001 | 0.000 | Acceptable
ASP11 | 400N ø25 |  | 5.93mm | 0.001 | 0.000 | Acceptable
ASP12 |  |  | 6.42mm | 0.000 | 0.000 | OK
ASP13 |  |  | 6.36mm | 0.000 | 0.000 | OK
ASP14 |  |  | 6.29mm | 0.004 | 0.000 | Acceptable
ASP15 |  |  | 5.86mm | 0.000 | 0.000 | OK
ASP16 |  |  | 6.13mm | 0.000 | 0.000 | OK

## Slide 11: A01_IP
Load case review
Loading Force: 200N (Loading lasting for 100ms)
Impactor : Φ80mm
Target:
1、No breakage
2、Glove Box keep in place
Loading Direction: Global –Z , At the middle of glove box in Y direction
Temperature: 23℃
1.3. Static glove compartment compression test
Point | X | Y | Z
Position | 2508.65 | 437.65 | 1362.94

## Slide 12: A01_IP
The max plastic strain is 0.037, less than the elongation of PP-TD20 (0.5).
There is low risk of failure.
Static glove compartment compression test result overview
Load | Target | CAE Result | Status
200N Φ80mm | Plastic strain＜0.5(PP-TD20) | Plastic strain=0.037 | OK

## Slide 13: A01_IP
Load case review
Loading: V=24.1km/h (ω=0.00863rad/ms)
Applicator size: D=165mm
Temperature: 23℃
Target:
Not exceeding 80g for a duration of 3ms
2.1 Head impact
D=165mm
M=6.8kg
3ms > 80g
65g ≤ 3ms ≤ 80g
3ms ＜ 65g

## Slide 14: A01_IP
Load case review
Point Number | X/mm | Y/mm | Z/mm
ASP01 | 2436.86 | -36.82 | 1735.00
ASP02 | 2436.86 | 143.18 | 1735.00
ASP03 | 2436.86 | 323.18 | 1735.00
ASP04 | 2436.86 | 483.18 | 1735.00
ASP05 | 2462.22 | -37.29 | 1654.05
ASP06 | 2462.22 | 142.71 | 1654.05
ASP07 | 2461.14 | 322.67 | 1657.42
ASP08 | 2463.68 | 483.18 | 1649.49
ASP09 | 2454.70 | 524.98 | 1688.43
ASP10 | 2408.69 | 642.98 | 1686.27
ASP11 | 2397.82 | 655.39 | 1589.21
ASP12 | 2448.64 | 632.69 | 1509.66

## Slide 15: A01_IP
All of the points can meet the target. And the red boxed area is exemption zone.
Head impact result overview
Point Number | Target | V00 | V01 | Status
ASP01 |  | 54.68 | 52.01 | OK
ASP02 |  | 57.10 | 52.49 | OK
ASP03 |  | 51.47 |  | OK
ASP04 |  | 49.69 |  | OK
ASP05 |  | 62.62 | 62.54 | OK
ASP06 |  | 87.67 | 78.55 | Acceptable
ASP07 |  | 80.30 |  | Acceptable
ASP08 |  | 91.12 |  | Acceptable
ASP09 |  | 76.37 |  | Acceptable
ASP10 |  | 104.80 |  | Acceptable
ASP11 |  | 105.59 |  | Acceptable
ASP12 |  | 97.80 |  | Acceptable
3ms > 80g
65g ≤ 3ms ≤ 80g
3ms ＜ 65g

## Slide 16: A01_IP
Load case review
3.1 NVH analysis
Target: Global Frequency > 35Hz
Temperature: 23℃

## Slide 17: A01_IP
1st Global Modal of IP&CNSL = 35.3Hz > 35Hz, and it can meet the target.
1st Global Modal of HSK = 40.0Hz > 35Hz, and it can meet the target.
Results overview of NVH analysis
Global Modal |  | Target | CAE Result / Hz | Status
 |  |  | V00 | 
IP&CNSL | 1st | Natural Frequency > 35Hz | 35.1 | OK
 | 2nd |  | 40.2 | 
 |  |  |  | OK
HSK | 1st |  | 40.0 | OK
 | 2nd |  | 40.2 | OK

## Slide 18: A01_IP
Load case review
3.4 Rear Impact
Loading: 30g Sine wave
Target:
1、The dashboard structure is complete
2、The dashboard can not detach from MQT
3、Cover and clip remain closed
Loading Direction: Global -X
Temperature: 23℃

## Slide 19: A01_IP
The load case of Rear Impact can meet the target.
There are only individual welding columns and ribs have detached, and there are no parts flying out.
Results overview of Rear Impact
Load case | Target | CAE Result | Status
Rear Impact | 1、The dashboard structure is complete | The IP structure and Wrap-around trim bracket is complete. | OK
 | 2、The dashboard can not detach from CCB | The connection points between IP and CCB have not fallen off | OK
 | 3、Cover and clip remain closed | The Glove box remain closed after impact, there are only individual welding columns and ribs have detached, and there are no parts flying out. | Acceptable

## Slide 20: A01_IP
Load case 3.6 review
Loading Acceleration: frequency Spectrum
Loading Direction: Global X Y Z
Temperature: 23℃
Target: Displacement<0.1mm
3.6 Image stability of FID and ABT
Response points

## Slide 21: A01_IP
All response points can meet the target.
Point | Load | Target | CAE Results |  |  | Status
 |  |  | X(mm) | Y(mm) | Z(mm) | 
ASP01 | frequency Spectrum | Displacement<0.1 mm | 0.00 | 0.00 | 0.01 | OK
ASP02 |  |  | 0.00 | 0.00 | 0.01 | OK
ASP03 |  |  | 0.01 | 0.01 | 0.01 | OK
ASP04 |  |  | 0.01 | 0.01 | 0.01 | OK
ASP05 |  |  | 0.00 | 0.01 | 0.01 | OK
3.6 Image stability of FID and ABT results overview

## Slide 22: A01_IP
All response points can meet the target.
Point | Load | Target | CAE Results |  |  | Status
 |  |  | X(mm) | Y(mm) | Z(mm) | 
ASP06 | frequency Spectrum | Displacement<0.1 mm | 0.01 | 0.01 | 0.00 | OK
ASP07 |  |  | 0.01 | 0.01 | 0.01 | OK
ASP08 |  |  | 0.00 | 0.01 | 0.01 | OK
ASP09 |  |  | 0.01 | 0.01 | 0.01 | OK
ASP10 |  |  | 0.00 | 0.01 | 0.01 | OK
ASP11 |  |  | 0.01 | 0.02 | 0.00 | OK
ASP12 |  |  | 0.00 | 0.02 | 0.01 | OK
ASP13 |  |  | 0.00 | 0.02 | 0.02 | OK
3.6 Image stability of FID and ABT results overview

## Slide 23: A01_IP
Load case review
3.2. Airbag deployment
Target:
1、The dashboard structure is complete
2、 Airbag safety deployment
3、Front Glass no failure
4、Cover and clip remain closed
Temperature: 23℃/-35 ℃ /85 ℃

## Slide 24: A01_IP
The load case of Airbag deployment RT can meet the target.
Results overview of Airbag deployment RT
Load case | Target | CAE Result | Status
Airbag deployment | Structure complete, no parts fly out | Upper and lower bracket structure is complete; Speaker cover、air outlet trim panel and upper atmosphere light cover have not fallen off. | OK
 | IP Structure of airbag area no failure | The max. plastic strain of upper bracket and upper cover are higher than the elongation of PP-LGF20(0.032) , there are minor damage in upper bracket and topper cover. | Acceptable
 | Front Glass no failure | Front Glass has no failure. | OK
 | Airbag deployment avoid the ICP, A-Saeule | ABT shake; Contact with A-Saeule when airbag deployment | Acceptable

## Slide 25: A01_IP
The load case of Airbag deployment HT can meet the target.
Results overview of Airbag deployment HT
Load case | Target | CAE Result | Status
Airbag deployment | Structure complete, no parts fly out | Upper and lower bracket structure is complete; Speaker cover、air outlet trim panel and upper atmosphere light cover have not fallen off. | OK
 | IP Structure of airbag area no failure | The max. plastic strain of upper, lower IP bracket and upper cover are higher than the elongation of PP-LGF20(0.063), there are minor damage in upper bracket and topper cover. | NOK
 | Front Glass no failure | Front Glass has on failure | OK
 | Airbag deployment avoid the ICP, A-Saeule | ABT shake; Contact with A-Saeule when airbag deployment | NOK

## Slide 26: A01_IP
The load case of Airbag deployment LT can meet the target.
Results overview of Airbag deployment LT
Load case | Target | CAE Result | Status
Airbag deployment | Structure complete, no parts fly out | Upper and lower bracket structure is complete; Speaker cover、air outlet trim panel and upper atmosphere light cover have not fallen off. | OK
 | IP Structure of airbag area no failure | The max. plastic strain of upper bracket and upper cover are higher than the elongation of PP-LGF20(0.034), there are minor damage in topper cover. | NOK
 | Front Glass no failure | Front Glass has on failure | OK
 | Airbag deployment avoid the ICP, A-Saeule | ABT shake; Contact with A-Saeule when airbag deployment | NOK